## Slide 1: Cornucopia: Temporal Safety for CHERI Heaps
N. “Wes” Filardo, Brett F. Gutstein, Jonathan Woodruff, Sam Ainsworth, Lucian Paul-Trifu, Brooks Davis, Hongyan Xia, Edward Tomasz Napierala, Alex Richardson, John Baldwin, David Chisnall, Jessica Clarke, Khilan Gudka, Alexandre Joannou, A. Theo Markettos, Alfredo Mazzinghi, Robert M. Norton-Wright, Michael Roe, Peter Sewell, Stacey Son, Timothy M. Jones, Simon W. Moore, Peter G. Neumann, Robert N. M. Watson Additional thanks to our dozens of non-author collaborators.
Notes: Hello everyone, I’m nwf, or Wes, one of a cast of many on the CHERI capability architecture project.
I’m going to present Cornucopia, our fully-elaborated design for temporal safety of CHERI-aware *nix user-space programs’ heaps.

## Slide 2: Overview
Memory Safety Trifecta
CHERI Architecture, *nix on CHERI, Sweeping Revocation
Instantiating the CHERIvoke Algorithm
Mostly-Concurrent Revocation
Assessing Correctness, Performance Results
Notes: That’s a bit of a mouth-full, so we’ll get there in stages.
First, I’ll say what we mean by ”memory safety.”
Then, a quick review of some earlier work: the CHERI architecture, what it looks like to port a *nix to it, and a surprisingly simple ”revocation sweep” strategy for temporal safety.
Foundations in place, we’ll implement that strategy in the *nix kernel and modify a malloc() to use it.
We’ll see that it’s straightforward to make our implementation do most of its work concurrently with the application.
Last, we’ll look at the measurements we took to assess correctness and performance.

## Slide 3: Memory Safety Trifecta
Pointer integrity (machine pointers “behave like” object references)
  Sound provenance; representation integrity.
  No: wild pointers, overwritten bit representations.
Spatial safety (machine memory “behaves like” objects)
  Objects have runtime size; pointers confer right to access (and may modulate access).
  Pointers carry bounds (& permissions); access rights are monotone non-increasing.
  No: use of a pointer outside its bounds (or beyond its permissions).
Temporal safety (machine encoding captures reachability and lifetime)
  Possible to get a “fresh” object, distinct from all others.
  All distinct, concurrently reachable objects do not overlap in memory.
  No: use of memory before allocation or after reallocated for other uses.
Notes: “Memory safety” is a difficult term to define precisely, and opinions differ, but we take it to have at least three aspects.
First, “memory safety” requires that we have notions of provenance and integrity of pointers: pointers come only from other pointers or more trusted components (such as the kernel) and pointers are immune from bit-level tampering.
Next, we must be able to carve memory up into “objects” that have defined location and size. We may access an object only if we have a pointer to it; having a pointer to an object does not give us access to neighboring objects.
And last, objects may have bounded lifetime. Newly constructed objects are distinct entities, even if they occupy reused memory. We must not hold a reference to an object before it is created and references must cease to be useful after memory is reallocated for another object.

## Slide 4: Memory Safety, Authority, and Capabilities
Conceptually, holding a pointer confers authority to access memory
Correspondence between safety properties and authorization:
Capability systems make authority explicit in bearer tokens.
  Capability revocation generally challenging, as is temporal safety in C.
Memory Safety | Authority
Integrity and Provenance | Unforgeability
Spatial Safety | Limits on Authorization
Temporal Safety | Revocation of Authority
Notes: Conceptually, holding a pointer confers authority to access memory, and there is a natural correspondence between the safety properties just outlined and authorization.
Pointer integrity and provenance mirrors the unforgeability of authority; spatial safety reflects limited authorization, and temporal safety corresponds to revocation of authority.
Capability systems use explicit bearer tokens to capture authority; in these systems, capability revocation is, like temporal safety in C, generally considered hard to implement without sacrificing performance.

## Slide 5: CHERI Architecture: Pointers become Capabilities
CHERI Architectural Capabilities (Watson et al., CHERI ISAv7, 2018).
  Architecturally-defined, “fat pointer” w/ one-bit OOB validity tag.
  Carry cursor, base, and top addresses (and permission and type bits).
  CPU enforces bounds and permissions checks on dereference operations.
  Overwriting a capability with data clears the validity tag.
  CPU instructions ensure no de-novo validity or enlarging of bounds.
CHERI composes with “host” ISAs: here, MIPS; but also RISC-V & Arm’s Morello.
Globals
Data
Heap
Stack
Code
Control flow
Monotonicity
Permissions
Integrity and provenance validity
Bounds
Notes: CHERI is a capability processor architecture designed to run C programs and yet enforce aspects of memory safety within the instruction set itself.
CHERI capabilities are 128-bit packed structures, pairing a traditional 64-bit integer address with upper and lower bounds. Moving the address out of bounds and dereferencing will trap rather than access memory.
By distinguishing between integers and references at the ISA level, we can begin to enforce provenance.
Capabilities can be copied and manipulated using dedicated instructions, but directly manipulating the bit representation of a capability turns it into data by clearing an out-of-band tag bit, making it no longer usable as a reference to memory.
The CHERI ISA does not offer mechanisms for setting the tag bit or enlarging the bounds of a capability without already holding a still-tagged capability that would encompass the result.
Thus, CHERI can readily enforce provenance and spatial aspects of memory safety.
CHERI composes with ”host” ISAs; Cornucopia was implemented atop the CHERI-MIPS architecture, but our work will port to CHERI-RISC-V and to Arm’s experimental Morello.

## Slide 6: CheriBSD and CheriABI
Making software use CHERI requires compiler, kernel, & RTS changes.
  CheriBSD is a fork of FreeBSD; we use LLVM/Clang for compilation.
Define new spatially-safe *nix ABI (Davis et al., CheriABI, 2019).
  Explicit pointers bounded to their underlying allocations (or tighter).
    Notably, malloc() returns pointers bounded to (padded) allocations.
Notes: Using CHERI’s enforcement possibilities required many but modest changes to runtime and systems software: the C/C++ compiler, operating system kernel, and runtime libraries (notably including the heap allocator) all had to be taught to use the CHERI protection mechanisms. The net result is a new, capability-based *nix ABI for spatially-safe user-space programs.
For our purposes, a key point is that malloc() returns pointers with bounds set to the allocated region and these pointers are the only way to access that memory from outside the allocator, which we take as part of the trusted computing base.

## Slide 7: Temporal Safety vs. CheriABI Programs
CHERI and CheriABI address integrity and spatial safety, but…
  CHERI capabilities self-contained; like traditional pointers, copied.
No inherent architectural or ABI support for capability revocation.
  CHERI avoids indirection for performance and μ-arch familiarity.
  Heaps in particular: malloc() callers can retain access past free().
That’s sad: 24% of MS CVEs 2006-2018 are UAF (Matt Miller, BlueHat IL, 2019).
  Goal: always-on defense, not just in test; requires performance.
Notes: CHERI and CheriABI address integrity and spatial protection, but CHERI capabilities are self-contained objects. Like integer pointers in traditional C implementations, CHERI capabilities are prolifically copied by CheriABI programs.
By design, CHERI does not require indirection to interpret its capabilities and the conceptual provenance tree is compressed to a single tag bit. These decisions increase performance and micro-architectural familiarity but challenge revocation. In short, applications can still retain copies of capabilities handed to free().
And so CheriABI risks not mitigating a large, often exploited class of vulnerabilities. We are after defenses sufficiently performant that they can be always-on, not just when debugging or testing.

## Slide 8: Heap Temporal Safety Threat Model
“Well-intended but buggy” application exposed to adversary which can
  Directly trigger malloc() and free()
  Read/write memory it allocated
Model of attacker with indirect heap manipulation (e.g., JS in sandbox)
Adversary wins if it holds a capability to re-allocated memory; we…
  Eliminate temporal aliasing of objects (no “use-after-reallocation”),
  May allow use-after-free, up until some point before reallocation.
  Attacks rely on aliasing, not merely use-after-free as such.
Defense can’t just leak memory.
Notes: We focus on the case of a “well-intentioned but buggy” application exposed to an adversary with direct access to malloc() and free() and to memory it has allocated, but we do not go so far as to permit arbitrary code execution. Roughly, our adversary is something like JavaScript running in a web browser sandbox.
The adversary wins if a capability it obtains from malloc() comes to point to another object’s memory. We must eliminate temporal aliasing of objects, what might be called use-after-reallocation, though we may permit some use-after-free so long as the memory has not yet been repurposed. That is, access to free memory might indefinitely continue to see the old object. Attacks rely on aliasing, not merely use-after-free, so this weaker defense still suffices.
Leaking memory on free()-s satisfies our requirements, but we rule it out.

## Slide 9: CHERIvoke Algorithm for Temporal Safety
CHERIvoke (Xia et al., CHERIvoke, 2019) considered a simple tactic:
  Accumulate free()-d memory in a quarantine buffer (like many systems before it);
  Before releasing memory from quarantine, delete (revoke) all pointers to it.
    Find and test (and NULL-out) every capability held by the program.
    Contrast CGs or MarkUs, which walk memory and mark allocations to keep.
Since quarantine may be scattered and have many discontiguous spans,
  CHERIvoke added a shadow bitmap: probe to decide fate of each capability.
Notes: In prior work, we assessed the feasibility of combining delayed reuse of memory with precise detection and removal of capabilities to free memory.
The CHERIvoke algorithm modifies heap allocators to collect free()-d memory in a quarantine state rather than immediately offer it for reuse. Once quarantine hits some size threshold, the application is paused, and all memory is swept for capabilities. Every capability found is assessed to determine if it points into quarantine and, if so, it is replaced with a trapping value (such as NULL).
The quarantine is, in principle, any subset of the heap; for maximum flexibility, CHERIvoke proposed the use of a shadow bitmap with a simple function to translate a pointer’s target to corresponding shadow bit. The allocator may keep quarantined regions in list form, but the sweep uses constant-time probes of the bitmap.

## Slide 10: Inside Cornucopia’s Allocator
Application allocates heap objects
  Pointed to by heap, stack, globals, regs, & kernel!
Application free()-s object, might retain references.
Risk: allocator creates new, overlapping object.
Instead: quarantine space, set bits in shadow.
  Cornucopia’s shadow is one contiguous block above the stack.
Eventually, ask kernel to sweep to revoke access.
  Revocation done by kernel: revoke held ptrs, access page metadata.
  Skip VM objects, pages, and cache lines w/o pointers.
Now safe to re-issue memory: no residual aliases.
  After clearing shadow to avoid unintended revocations.
Thread registers
Kernel
Stack
Globals
Heap
Shadow
Address Space
Shadow bitmap
Notes: So, all told, what does this look like?
An application makes allocation requests from malloc() and propagates the returned pointer to other locations on the heap or on the stack, into registers, or even into the kernel itself.
An application might retain references to a heap object after free()-ing it, and the underlying risk, absent enforced temporal safety, is that the allocator may create a new, overlapping object.
Instead, CHERIvoke/Cornucopia’s allocator quarantines the free space and sets bits in the shadow. Cornucopia takes the shadow to be a contiguous block of virtual address space corresponding to the entirety of user memory. (The allocator obtains access to the shadow via a system call.)
Eventually, the allocator requests that the kernel sweep memory and ensure that no capabilities pointing into quarantine remain. When the sweep is finished, the memory is safe to reuse and the allocator clears the shadow bits and puts memory back in its free list.

## Slide 11: Architectural Support for Revocation Sweeps
Revocation relies on CHERI’s ability to precisely identify capabilities!
  Rude to delete things that aren’t, but look like, pointers!
CLoadTags instruction lets sweep skip cache-lines with no capabilities.
Added prefetch to our cache fabric, unrolled revocation loop.
CHERI-MIPS has per-page option to trap on capability stores.
  Kernel can use to track which pages certainly do not hold capabilities.
    Introduces a notion of “capability-dirty” pages.
  PTW architectures can mutate PTEs directly, rather than trap.
CHERI has no overt, direct support for revoking access to memory, but…
Notes: As said, CHERI and CheriABI seemingly have no overt support for temporal safety or capability revocation, thus the need to sweep memory. However, we find that it is an effective substrate for this sweep, especially with some modest tweaking.
At its core, revocation requires that we be able to tell with certainty what is and is not a capability; CHERI tag bits answer this question precisely and without any extra data structure lookups.
CHERIvoke proposed, and we have added, a CLoadTags instruction in CHERI-MIPS, so that we can read an entire cache-line’s worth of tags at once, before we pull the line itself into cache. This lets us skip lines that do not have capabilities without perturbing the caches or going to DRAM for the line contents.
For lines that do contain capabilities, we have added way-restricted prefetching operations to our cache fabric and unrolled the revocation loop to overlap prefetching with revocation.
At larger scope, we have repurposed a long-standing protection feature in CHERI-MIPS, where pages can be marked as raising traps on tagged capability stores. In Cornucopia, the kernel observes when pages come to hold their first capability; to first approximation, the trap handler updates metadata and allows all subsequent capability stores to go ahead without traps.

## Slide 12: Cornucopia’s Revocation Service, Take 1
Suspend all other threads in the program.
Visit memory:
  For each VM object in the address space,
    If this object is not permitted to store capabilities, skip it.
    For each page in this object,
      If the page has no capabilities, skip it.
      For each cache line,
        If CLoadTags says it has no capabilities, skip it.
        For each capability, probe the bitmap and revoke if set.
      If we did not find any capabilities that survived revocation, mark this page as clean.
Ransack kernel hoards of capabilities
  Thread register files (trap frames), event cookies, …
Resume all other threads in the program and return to user-space.
Notes: So, with those ingredients, our initial implementation of Cornucopia’s revocation sweep begins with a barrier to suspend all other threads in a program. With the world stopped, we examine every capability to which the application has access.
The bulk of the time and effort goes into examining application memory. Here, we take advantage of being in the kernel to quickly skip over regions of the address space that are unmapped or that are forbidden from containing capabilities. Within mapped regions, we use capability-store tracking to skip over pages not containing capabilities. And within pages, we use CLoadTags to skip over cache lines. When we find a capability, we probe the bitmap and replace it with a trapping value, such as NULL.
Besides memory, we must examine some additional state: the thread register files, conveniently stored as trap frames, must be examined, as must any other places where the kernel stores capabilities for userland’s use. Each such subsystem requires a little bit of specialized code.
With all state examined, any other threads are resumed and control is returned to user-space.

## Slide 13: Cornucopia’s Revocation Service, Take 1
Sweep walks all of application memory, somewhat like a GC.
Sweep is cache friendly:
  Within each page, lines loaded in order (with CLoadTags hinting μarch).
  No pointer chasing.
  Bitmap probes are random, but to small data.
Notes: While we do, indeed, visit all (capability-bearing) application memory, like a GC, it’s worth emphasizing that our sweep is much friendlier to caches. We stride predictably within pages rather than chasing pointers in a graph walk, and, while bitmap probes are random, the shadow bitmap is quite small.

## Slide 14: Take 2: Mostly-Concurrent Revocation
Suspending all application threads for the entire sweep is not great.
Insight borrowed from VM migration and “mostly concurrent GC”:
  Multiple passes, each reducing the work for the next.
Distinguish pages already checked vs. modified since last visit.
Re-purpose arch. trap on capability stores after each visit.
  Trap is under software control, not tied to capability presence.
Notes: The requirement that we suspend the application for the entirety of the revocation sweep is not stellar; memory is big and even with our architectural assists, sweeping takes a long while.
Instead, we borrow a key insight from GCs and VM migration: take many passes, each hopefully reducing the work required later.
For us, that means distinguishing pages that have already had all their capabilities checked from those that have had new ones stored since last visit.
We achieve this by resetting visited pages to trap on capability stores, just as we do to track capability flow to pages without capabilities.
This trapping behavior is not architecturally tied to the presence or absence of capabilities; it’s just a behavior under system software control and so we can repurpose it.

## Slide 15: Take 2: Mostly-Concurrent Revocation
Revised revocation algorithm now uses two phases:
  Visit all pages w/ capabilities once concurrently with app running.
  Stop the world and revisit only modified pages.
Quarantine set changes over time:
  Each revocation must visit all pages w/ capabilities
  Even if not modified since the last revocation
Notes: The net result is that we can split revocation sweeps into two phases.
In the first phase, we visit all capability-bearing pages concurrently with the application, being careful that any application store of a capability to the page will cause us to revisit it later.
In the second phase, we stop the world and visit all pages modified since their last visit.
Because the set of memory in quarantine changes over time, revocation must visit all capability-bearing pages each time, regardless of modification.

## Slide 16: Checking Correctness
Used Juliet Test Suite’s corpora for
  CWE 415 (“Double Free”): 818 test programs
  CWE 416 (“Use After Free”): 393 test programs
All tests exhibited violation of temporal safety without Cornucopia.
All tests aborted, as desired, with Cornucopia, when we …
  Set quarantine to 0, to trigger revocation every free()
  Adjusted free() to abort, rather than no-op, on double-free
Notes: To check that Cornucopia does the right thing, we used the Juliet test suite’s corpora of double-free and use-after-free examples.
As expected, all tests exhibited violation of temporal safety without Cornucopia.
With Cornucopia, all tests aborted, so long as we set the quarantine size to 0, triggering revocation immediately on every free(), and also adjusted free() to abort on, rather than silently ignore, double-free. While these are not our usual operating parameters, this nevertheless demonstrates efficacy of our revocation sweeps.

## Slide 17: State-of-the-Art Runtime Overheads
CHERI-compatible SPEC CPU2006 benchmarks
  Without second thread, geomean is 5.8% (worst 26.2%).
  With second thread and core, geomean 1.9% (worst 8.9%).
  When offloading, pause times 10-20% of single-thread sweep typical.
Applications unmodified beyond existing small patches for CheriABI compatibility.
Notes: On CHERI-compatible SPEC CPU2006 integer benchmarks, Cornucopia’s single-threaded implementation achieved a geomean of 5.8% overhead. With a second thread (and a dual-core CPU), that dropped to less than 2%. When offloading, the world was generally stopped only 10-20% of the single-threaded sweep time.
Notably, applications were unmodified relative to their CheriABI ports. We ran them under a Cornucopia-supporting kernel and used LD_PRELOAD to shim a replacement malloc over libc’s.

## Slide 18: Memory Occupancy Overheads
Generally: reasonably close to target, w/ some outliers.
  MT/MP requires more memory due to allocations made during sweep.
  hmmer, omnetpp appear to tickle reuse issues in underlying allocator.
Notes: In terms of memory occupancy overheads, generally, Cornucopia manages to hold to its a priori chosen target of 33%. When using a second thread and offloading, Cornucopia overshoots a bit due to allocations made during the concurrent sweep, which can be satisfied only by growing the heap.
The bzip2 and sjeng workloads do not really avail themselves of malloc and so do not rise to threshold, while hmmer and omnetpp appear to go through distinct phases and cause our underlying malloc implementation to not reuse memory as aggressively as one might wish.

## Slide 19: DRAM Traffic Overheads
Cycle times aren’t everything. DRAM traffic is power-hungry.
Most workloads showed relatively little perturbation (0-5%).
  Heap size matters less than churn rate.
Allocator heavy workloads…
  15-30% overheads for single-threaded revocation; 30-45% for offloaded.
  5-10% overheads for mere act of quarantining; bad malloc placement policy?
Notes: Beyond cycle times and memory occupancy, a very important (if under-reported) metric is memory traffic overhead.
Most of the benchmarks tested showed very modest traffic overheads of 0 to 5%, but workloads that thrashed the allocator showed 15-30% overhead when using the inline Cornucopia revoker. Switching to concurrent revocation raised those further to 30-45%, as pages were revisited and the concurrent pass itself necessarily increased cache contention.
Interestingly, for these thrashing workloads, we see that merely quarantining accounts for somewhere between 5 and 10% of the overhead. This suggests that we may be intermixing objects of different lifetimes within cache lines, decreasing the utility of our caches.

## Slide 20: Other Things In The Paper
Details galore
Discussion of two allocators modified & generic wrapper developed.
Deeper analysis of costs of revocation
Releasing quarantined pages back to system (fewer sweeps!)
Multiple allocators within an address space:
  Secure access to the shadow space
  Light-weight synchronization for revocation work sharing
Notes: If you’re still curious for more, our paper goes into much more detail.
We include discussion of three different user-space components we developed and considered, a deeper analysis of where revocation incurs expense, and several considerations for future work and deployment of Cornucopia.
We simulated releasing quarantined pages back to the operating system to reduce the need for sweeping.
And last, the paper details mechanisms for secure and efficient operation of multiple allocators within a single program.

## Slide 21: Cornucopia: Temporal Safety for CHERI Heaps
Sweeping revocation seems within engineering effort of practicality.
Temporal safety historically considered expensive, but
  atop spatial safety, seems like it does not have to be.
  first? noted by (Zhang et al., BOGO, 2019)
Soon: deployable temporally-safe heap for CheriABI?
  Ongoing work to lower pause times and DRAM overhead.
Notes: We believe that sweeping revocation is within engineering effort of practicality and that there are some relatively straightforward steps we can make to lower the overheads reported here.
We can confirm the observation made by BOGO: while temporal safety has historically seemed expensive to achieve, being able to leverage spatial safety brings the costs down.
We are pursuing a new sweeping strategy that should address our worst overheads and, simultaneously, we are aiming to land in mainline CheriBSD so that, soon, every CheriABI program can enjoy heap temporal safety.
And with that, I’ll take questions.

## Slide 23: Memory Occupancy Overheads
We chose a target memory overhead of +33% of heap (dashed)
  CHERIvoke performs fewer sweeps if it is allowed a larger quarantine.
  We report peak RSS: includes both heap growth and pages for shadow bitmap.
    Baseline for us is CheriABI build w/o Cornucopia.
    There are caveats on these comparisons: much harder to assess memory impact than cycle time!
    BOGO not shown because it has nearly +0% overheads relative to llvm-mpx.
Notes: CHERIvoke has its quarantine size as a tunable parameter. We, somewhat arbitrarily, chose to set our threshold at quarantine being 25% of the total heap size, which gives an expected 33% gain in peak memory size.
We measure peak RSS, which includes pages for both the heap and the shadow bitmap (as well as the program text and global data). While there are caveats on the comparability of numbers reported for other systems, we see that Cornucopia is at least competitive.

## Slide 24: State-of-the-Art Runtime Overheads
Can also compare against Boehm-GC and ASAN.
  Caveat: these are MIPS versions, not CHERI-MIPS, so is not completely fair.
Cornucopia…
  Does not instrument code and allows some slack (unlike ASAN)
  Never guesses about when it needs to sweep (unlike GCs)
Notes: For comparison, we also ran MIPS versions of ASAN and Boehm-GC on our CHERI-MIPSplatform. We see that Cornucopia offers substantially better performance, though of course it is solving a different, if related, problem than either of these tools.
Beyond its use of CHERI and the slack of allowing some use-after-free accesses, Cornucopia’s performance advantage comes from having no need to execute instructions outside the allocator or kernel (leaving the bulk of runtime behavior unaltered) and from having explicit free information provided by the application.

## Slide 25: Sweep Frequency and Pause Times
Sweep frequency ranges from never to every 5 billion application cycles.
Full sweeps between 10 million and 1 billion cycles for 12 to 623 MB RSS.
When offloading, we see that full sweeps are very slightly longer, but…
  The world-stopped second phase is generally only 10% of the time.
Notes: Two interesting metrics are how often a workload exhausts its quarantine and how long it takes to revoke once it has. Our most aggressively allocating workload triggers a revocation every 5 billion application cycles. We find that a full sweep of memory takes between 10 million cycles for a 12 MB RSS and a billion cycles for 623 MB RSS.
Measuring per-sweep time, we can confirm that two-pass revocation usually spends just about 10%-20% of the time for a full sweep with the world stopped.

## Slide 26: Towards Always-on Temporal Defenses
Cornucopia is a great start, but not quite ready for prime time:
  Our pause times are still too large, even with incremental sweeps
  Our worst-case DRAM traffic overheads are still too high
  Our RSS usage is too unpredictable
Some of this is just engineering